## Slide 1
Introduction to Voyage Management System
NN220-09
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series -VMS Operator’s Manual (avalable electronically within the VMS Help Menu)

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - UNDERSTAND the Display and Basic Functions of VMS. a. Sensors data and display (SOG, STW, HDG, COG, MOB etc.) 2 - UNDERSTAND the sensor sources and identify valid and invalid sensors. 3 - UNDERSTAND all toolbars and Main Menu options. 4 - UNDERSTAND and set up all Feature Settings IAW SEANAV Navigation Standards. 5 - USE GoTo to move to different locations on VMS. 6 - IDENTIFY and load a chart, and understand chart scales. 7 - UNDERSTAND anchoring procedures and considerations. 8 - UNDERSTAND Critical Points, how to input them, and when they should be utilized. 9 - IDENTIFY Chart categories used in VMS and know how to read a DNC name. 10 - OPERATE Various Navigation Tools. a. Perform Man-Overboard Procedures b. Lines of Position c. Anchoring

## Slide 4
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
11 - OPERATE appropriate settings in the Safety Configuration Menu. 12 - USE Query Chart function. 13 - USE chart menu to create a new layer. 14 - ESTABLISH visual and RADAR NAVAIDS by creating a Layer under Manual Chart Update. 15 - USE the Route Editor to create, and save a Route Plan/NAV Plan. Enter Critical Points to coincide with Required Actions/Reports 16 - MAKE chart corrections to a digital nautical chart (DNC). 17 - EXPLAIN & Identify the Cross Track Error. 18 - LOAD a Route Plan. 19 - CREATE, save, load, start, stop and clear a Navigation Plan. 20 - UNDERSTAND the functions of Route Monitoring.

## Slide 5
VMS Main Display
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 6
VMS Main Display
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 7
VMS Upper Toolbar
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 8
VMS Upper Toolbar
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 9
VMS Lower Toolbar
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 10
VMS Lower Toolbar
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 11
VMS Main Menu and SubMenu
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Hovering the mouse over “Show Menu” will bring up the “Main Menu”
Selecting any item in the “Main Menu” will bring up that item’s “Submenu”

## Slide 12
VMS Sensor Information
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Primary Sensor Information
  Heading, Course Over Ground, Speed Through the Water, Speed Over Ground, Vessel Depth, and Position
  When active, these sensors should appear green with selected sensor indicated on the right.
Sensor Submenu
  Can view/change the source of information for specific sensors.
  Can also view sensor source by clicking on the sensor information on the upper and lower toolbars.
Valid Sensors: GREEN
Degraded Sensors: YELLOW
Invalid Sensors: RED

## Slide 13
VMS Alarm Announcements
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
3 Categories
  Alarms
  Warnings
  Cautions
Accesses in upper toolbar or alarm submenu

## Slide 14
VMS Alarm Announcements
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
3 Categories
  Alarms
  Warnings
  Cautions
Accesses in upper toolbar or alarm submenu

## Slide 15
VMS Man Overboard
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
To enter a man overboard, select the “Man Overboard” icon on the upper toolbar.
The MOB icon will be orange while the man overboard is active:
The “Man Overboard” pop-up window will provide necessary information for recovery and can be manually adjusted.
VMS automatically solves for Set and Drive to aid in recovery.

## Slide 16
VMS Navigation Plans
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
We use the many functions of VMS to aid in voyage planning
Our ultimate goal is to create a Navigation Plan in the system for watch-standers to follow on the bridge.
A Nav Plan in VMS has three primary components:
  Charts (what area we are operating in)
  Layer (customization of the area)
  Route (how we will travel through the area)

## Slide 17
Developing a NAV Plan
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Set Chart Settings, Dangers and Safety Parameters
Center chart display on the area you will be operating
Record required DNCs (charts) for route
Create a Layer (customize the area)
  NTM updates if cannot be applied through a VDU
  Navigation Aids to be used for Visual/RADAR LOPs
Create a Route
  ETA/ETD
  Critical Points
Create an Anchorage (if applicable)
Create a Navigation Plan

## Slide 18
Units of Measure
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
While preparing our chart, we want to ensure our information aligns with our display.
Units of measure can be changed by selecting “Options” in the “System” submenu.
  Our default unit for “Depth” and “Height” is “Foot”
  Our default unit for “Position” is DD°MM’SS”
The “Foot/Meter” button on the upper toolbar allows us to display either English or Metric Units
  Our default is “English Units”

## Slide 19
Chart Settings
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
We alter our Chart Settings by selecting the “Base/STD/Other/Custom” button on the upper toolbar. Chart Settings are divided under two tabs: “Features” and “Symbology”
  Our default display mode under “Features” is “Custom”
  Our default “Custom Display Setting” is “All”
  Our default “Symbology” is “All”
  Our Default “Text Scale” is “1.0”

## Slide 20
Safety Parameters
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
In order to avoid groundings and collisions, we develop a 3-D Box which moves with the ship called “Own Ship Safety Region.”
The Box extends ahead of the Ship to a distance determined by Speed and “Look Ahead Time”.
The values require to be input to create this region are:
  Look-Ahead Time (similar to DR)
  Added Breadth
  Safety Depth
  Safety Height.
VMS alarm if our course crosses a danger that falls within set parameters.

## Slide 21
Own Ship Safety Region
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Look-ahead time
  As prescribed in NAVDORM
  2x Fix Interval
Added Breadth
  Ship’s beam width
Safety Depth
  Equal to Navigational Draft specified in Ship’s characteristics
  Usually Ship’s maximum draft plus 10% or as ordered by CO for safety
  Detailed in Ship’s NAVBILL
Safety Height
  Height of Mast + (as per common practice) 25 feet
  Applies to all Ships regardless of class.
Alarm on Cautions
  “ON”

## Slide 22
NAVDORM Settings

## Slide 23
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Safety region values are entered in two areas: “Dangers” and “Chart Depths/ Heights”
Both pop-up windows are accessed in the “Charts” submenu.
The “Dangers” pop-up window can also be accessed on the upper toolbar.
Own Ship Safety Region

## Slide 24
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Example
Ship’s Characteristics
  Draft: 31 feet
  Navigation Draft: 36 feet
  Height of Mast: 160 feet
  Beam Width: 55 feet
  Height of Eye: 60 feet
  Ship Length: 567 feet
  = Safety Depth
  + 25 feet = Safety Height
  = Added Breadth

## Slide 25
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Brilliance
We are able to adjust the VMS display’s brilliance for different lighting conditions.
We can access our brilliance options by selecting the brilliance icon on the lower toolbar or through the brilliance sub-menu.

## Slide 26
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Moving the Chart Display
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?

## Slide 27
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Chart Display Scale
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
We can manually adjust the chart display scale on the upper toolbar.
Using the directional arrows on either side of the current scale will adjust the displayed scale.
Clicking on the current scale will display the chart scale drop-down menu, and we can select the desired scale.
We can also zoom on a specific area by right clicking on the display and selecting “Zoom Here.”
  A dotted, adjustable box will appear around the desired area.

## Slide 28
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Charts in VMS
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To access the available chart database, select the “Charts drop-down menu” on the upper toolbar.
The Navy uses DNCs, so ensure you have the appropriate chart(s) selected.
There are four categories of DNCs based on chart scale:
  General (small scale, large area)
  Coastal
  Approach
  Harbor (large scale, small area)

## Slide 29
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Charts in VMS
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?

## Slide 30
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Required Charts
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Once your display is centered on the desired area, the “Charts drop-down menu” will list all the available charts.
Ex: San Diego Harbor (32-40N; 117-14W)
  DNCs Required:
  Harbor  H___________
  Approach  A___________
  Coastal  COA_________
  General  GEN_________
  1316010
  1316010
  13B
  13A

## Slide 31
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
How to Read a DNC
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
How to read a DNC: H1316010
  H: Scale (Harbor)
    Could be Harbor (H), Approach (A), Coastal (COA), or General (GEN)
  13: DNC Region (13 of 29 DNC regions)
    Could be any region from 01-29, see DNC regional map
  16010: World Port Index (WPI) Number
    Affiliated to a specific port
  Can search any WPI here
  http://msi.nga.mil/NGAPortal/MSI.portal?_nfpb=true&_pageLabel=msi_portal_page_62&pubCode=0015

## Slide 32
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
DNC Regions
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?

## Slide 33
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Chart Query
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
For information about individual objects on a chart display, we conduct a “Chart Query.”
Selecting the “Query” button on the Lower Toolbar opens the “Chart Query” pop-up window
  Click the “Query Off” button to activate the query. The Cursor will change to the query shape and the label will change to “Query On.”
We can conduct a query directly on the display by right clicking the area we wish to query and selecting “Query Chart.”

## Slide 34
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Developing a NAV Plan
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Set Chart Settings, Dangers and Safety Parameters
Center chart display on the area you will be operating
Record required DNCs (charts) for route
Create a Layer (customize the area)
  NTM
  Navigation Aids
Create a Route
  ETA/ETD
  Critical Points
Create an Anchorage
Create a Navigation Plan

## Slide 35
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Create a Layer
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
We create a layer to customize our display for specific evolutions or in a response to an update.
Examples of what we include in a Layer include:
  Navigation Aids
  Notice to Mariners (NTM)
To create a new Layer:
  “Show Menu”  “Charts”  “Manual Chart Update”
  In the pop-up window, select the “Layers” tab
  Type in desired layer name and select “Add New Layer”
Create a Layer and name it “NN220x_Last Name”

## Slide 36
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Manual Chart Updates
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To ensure your layer is the only one on your display, select the “Display” tab and the Displayed Layers are shown.
Click a layer from the list to select/ deselect the layer.
Layers with a check mark will be visible on your display.

## Slide 37
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Edit a Layer
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
The navigator will choose objects and features in the area to serve as navigation aids.
  The list of navigation aids is called a Gazetteer
  Refer to Coast Pilot or Sailing Directions for commonly used navigation aids
Input Navigation Aids
  Select “Edit” tab in Manual Chart Update pop-up window  Select “New Object”
  Select desired layer in drop-down “Layer” menu (your layer)
  Select object category in the drop-down “Type” menu
  Select the appropriate symbol in the drop-down “Symbol/description” menu
  Select “Manually Create”
(Continued next slide)

## Slide 38
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Edit a Layer
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Manually Create
  The pop-up window will refresh with more options for us to fill out.
  We have already filled out “Layer,” “Type,” and “Symbol/Description.”
  Enter desired position for the object and any notes and labels associated with the object in the appropriate tabs.
  Name the object (in accordance with your gazetteer)
NTM
  If an object is added/ updated in response to a Notice to Mariners, selecting the “Advanced” button will allow us to properly associate the NTM by week and year.
Select “Done” to add the object to your layer.

## Slide 39
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Example
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Layer Name: NN220x_Last Name
Gazetteer:
  VA: 32° 41’ 31” N
  Tower 117° 15’ 04” W
  VB 32° 42’ 05” N
  Tower 117° 12’ 28” W
  RA 32° 41’ 57” N
  Pier 117° 14’ 15” W
  RB 32° 39’ 53” N
  Pt Loma 117° 14’ 33” W

## Slide 40
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Create a Route
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
We create a route to consolidate the track, establish turn bearings and ranges, set reminders for significant events, and monitor dangers along our track.
Once the CO approves a route, the navigation team monitors it continuously throughout a transit.
To create a new route:
  “Show Menu”  “Routes”  “Edit Route”
  In the pop-up window, select the “Route” tab
  Select “Clear/New”  “Save As”
    Type in desired route name  “OK”
Create a route and name it “NN310_Lastname”
  We can set the “ETD.”
  “Total Distance and Duration” and “ETA” are calculated based on the waypoint information

## Slide 41
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Create Waypoints
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To create Waypoints for a route:
  Select “Wpts” tab in Edit Route pop-up window
  Select “New”
    Type in desired latitude and longitude
    Fill in desired speed, off track limit, and rudder angle for approaching leg, turn, and departing leg in accordance with track data sheet
  Select “New” to continue with next WP.
    The next WP will always initially appear directly on top of the proceeding WP.
    Repeat steps as necessary.
  Once all WPs have been created, select “Save”

## Slide 42
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Create Route Features
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Turn Bearings and Ranges
  Select “Features” tab in Edit Route pop-up window and select desired waypoint
    Ex. Turn Bearing on leg 3-4 will be taken at WP4
  Select the turn icon
    Fill in information for desired turn bearing/range object.
    Right-clicking in the position field and select “Query” to choose turn objects on your display.
    Verify correct object in pop-up window and select appropriate aid and select “OK”
    Type in desired name and select “New” once you are finished.
    Select “Save” after all turn bearings and ranges are entered.

## Slide 43
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Example
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Route Name: NN220x_Lastname
Track Data Sheet

## Slide 44
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Creating a Great Circle Route
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
-VMS gives us the ability to plot a Great Circle route over long distances to show the shortest distance between two points on a sphere.
-This is useful in trans-oceanic voyages.
-However, a Great Circle route is impractical to navigate.
-What is the solution?

## Slide 47
Divide route into legs, no more than 350-400 NM each.
Change each of the legs from GCs to RLs.

## Slide 48
155◦
150◦
145◦
140◦
135◦
130◦
125◦
120◦
160◦
45◦
40◦
35◦
30◦
25◦
20◦
50◦
Essentially, you’ve broken up a Great Circle track into smaller legs using Rhumb Lines to form a Composite Track.
This allows for steadying courses, while still driving the shortest distance.
Rhumb Line 2280 NM
Composite Track 2270 NM

## Slide 49
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Critical Points
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Critical Points (CP) are special events along a route that require those on watch to take action. The navigator creates CPs based on proximity (time or distance), and will generate an alarm or warning at the proximity. Examples include:
  Crossing the Line of Demarcation
  Pilot Pick-up
  Station Sea and Anchor Detail

## Slide 50
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Critical Points
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To create CPs:
  Select “CP” tab in “Edit Route” pop-up window
  Select “New”
  Type in desired latitude and longitude of critical point
  Select appropriate Alert Type and enter desired proximity
  Type in desired Description prompt
  Repeat steps as necessary.
  Select “Save”

## Slide 51
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Route Dangers
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
VMS identifies dangers and cautions along a planned route.
  Select “Dngrs” tab in Edit Route pop-up window
  Select desired leg
  Select scale (recommend largest scale available)
If there are too many dangers to process
  Check your route! You may be going through shoal water or over land!

## Slide 52
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Route Monitoring
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Once our route is created and saved, we can monitor the route for real-time information
To monitor your route:
  “Show Menu”  “Routes”  “Monitor Route”
Load your route and the window will provide information such as:
  Bearing (course)
  Distance and time to turn
  Information on the following course
  Cross-track error
  Turn bearing information
  And many more functions

## Slide 53
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Anchoring
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To input an anchorage area.
  “Show Menu”  “Nav Tools”  “Anchoring”
  Select “Planning” tab in Anchoring pop-up window.
  Type in desired latitude and longitude of anchor position or select “On Chart”
    Selecting “On Chart” will change the cursor to select location display. Click on the display at desired area to set the location.
  Select “On Chart” button for Head brg and click desired aid
  Type in desired latitude and longitude for appropriate aids under Drop Objects range and bearing or select “On Chart”
  On chart zoom in at anchorage position.
  Record nearest charted depth and type in at Anchor Depth.
  Select desired Anchor Scope of chain.

## Slide 54
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Example
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Anchorage
  32° 43′ 06“ N
  117° 11′ 00“ W
Head Bearing
  VB
Drop Bearing
  RB
Drop Range
  RB
Amount of Chain 5x

## Slide 55
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Anchoring
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
How to monitor your anchorage
  Select “Status” tab in Anchoring pop-up window.
  Select “Anchoring Feature On.”
Values for drop bearing and drop range are found in “Reference Drop Objects.”
Once ship is ready, selecting “Drop Anchor” will initiate the process in VMS.
NAVDORM:

## Slide 56
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
VMS Drag and Swing Circle
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Drag/Swing circles smaller than what normally plotted on paper chart due to scope or catenary on the chain
Alarm as ship approaches edge of drag circle
VMS “Anchor chain”
Actual Anchor chain

## Slide 57
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Navigation Plan
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To create a new navigation plan
  “Show Menu”  “Nav Plans”  “View/Edit Nav Plan”
    In “NP” tab select “Modify” button at bottom of the “View/Edit Nav Plan” pop-up window.
    Select “Create” button.
    Type in NN310_Lastname and select “Okay”
To associate your route, layer, and charts
    In “Rte/PIM” tab select “Insert” button.
    Select desired route.
    Repeat steps in “Lyr” and “Cht” tabs.
    Must select all four DNCs in “Cht” tab.
    Save NavPlan

## Slide 58
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Example
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Navigation Plan Name: NN220x_Lastname
  Layer: NN220x_Lastname
  Route: NN220x_Lastname
  Charts: H1316010
      A1316010
      COA13B
      GEN13A

## Slide 59
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
VMS Piloting
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
“Goto” the following location
  Lat: 32°40’000” N
  Lon: 117°14’000”W
Display your layer
Open the menu that allows you to select the sensor for ship’s position (remember how?)
Select “Man” for sensor
Manually input ship position
  32°42’00”N
  117°13’55”W

## Slide 60
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Selecting NAVAIDs
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Open “Line of Position” pop-up window
  “Show Menu”  “NavTools”  “Line of Position”
Select the “Local Navaids” tab to begin an automatic chart query of available NAVAIDs
Select which NAVAIDs you want to use for your fix by clicking the check box next to each available NAVAID
Select “Activate Selected LOPs”

## Slide 61
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Creating a Line of Position
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
All selected NAVAIDs will populate under the LOP tab
Manually
  Select “Manual” from the drop-down menu next to desired NAVAID
  Enter manual bearing/ range
Automatically
  Select “Predicted” from the drop-down menu next to desired NAVAID
  The system automacially fills in bearing/ range

## Slide 62
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Calculating a Fix
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
Click the “Calc Fix” button on the bottom of the LOP menu
Enter in quality of fix based on “Difference” box.
  Difference display shows the difference between the calculated LOP position and the active sensor value.
Accept fix to display the fix on your chart
Reject the fix to reset the LOP menu

## Slide 63
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Route Monitoring
We can offset the chart left, right, up, or down by clicking near the edge of the chart display (the cursor will change into an arrow).
To center the chart on a specific position, select “Goto” on the lower toolbar to open the “Goto” pop-up window.
Enter desired latitude and longitude and select “Go” to offset the chart display on the position.
Enter the following coordinates:
  Lat: 32°40’000” N
  Lon: 117°14’000”W
What area is your chart now centered on?
To monitor your route:
  “Show Menu”  “Routes”  “Monitor Route”  “Load Route”  Select your route.
Input manual COG, Heading, and SOG to view how the values change.

## Slide 64
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 - UNDERSTAND the Display and Basic Functions of VMS. a. Sensors data and display (SOG, STW, HDG, COG, MOB etc.) 2 - UNDERSTAND the sensor sources and identify valid and invalid sensors. 3 - UNDERSTAND all toolbars and Main Menu options. 4 - UNDERSTAND and set up all Feature Settings IAW SEANAV Navigation Standards. 5 - USE GoTo to move to different locations on VMS. 6 - IDENTIFY and load a chart, and understand chart scales. 7 - UNDERSTAND anchoring procedures and considerations. 8 - UNDERSTAND Critical Points, how to input them, and when they should be utilized. 9 - IDENTIFY Chart categories used in VMS and know how to read a DNC name. 10 - OPERATE Various Navigation Tools. a. Perform Man-Overboard Procedures b. Lines of Position c. Anchoring

## Slide 65
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
11 - OPERATE appropriate settings in the Safety Configuration Menu. 12 - USE Query Chart function. 13 - USE chart menu to create a new layer. 14 - ESTABLISH visual and RADAR NAVAIDS by creating a Layer under Manual Chart Update. 15 - USE the Route Editor to create, and save a Route Plan/NAV Plan. Enter Critical Points to coincide with Required Actions/Reports 16 - MAKE chart corrections to a digital nautical chart (DNC). 17 - EXPLAIN & Identify the Cross Track Error. 18 - LOAD a Route Plan. 19 - CREATE, save, load, start, stop and clear a Navigation Plan. 20 - UNDERSTAND the functions of Route Monitoring.

## Slide 66
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy