## Slide 1
Preparations for Getting Underway
NN220-12
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation– Updated May 2023
SEANAV I United States Naval Academy

## Slide 2
References
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The American Practical Navigator, Pub. No. 9, Bowditch, VOL. 1, 2019 Edition -Surface Ship Navigation Department Organizations and Regulations Manual (NAVDORM), COMNAVSURFPAC/COMNAVAIRPAC/COMNAVAIRLANT/COMNAVSURFLANT INSTRUCTION 3530.4 series

## Slide 3
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – DESCRIBE the following operational messages: LOGREQ, WEAX, and MOVREP. 2 - UNDERSTAND the impact of hazardous weather conditions on surface and flight operations. 3 – DESCRIBE different weather fronts and the difference between high and low pressure systems. 4 - DESCRIBE the importance of understanding Tides and Currents. 5 - DESCRIBE the causes of tides. 6 - DESCRIBE the two main types of currents and the two main types of tidal currents. 7 - DESCRIBE the different types of watch conditions. 8 - DETERMINE the appropriate watchstanders needed for Restricted Waters, Piloting Waters, Coastal Waters and Open Ocean Transits IAW the NAVDORM. 9 - DEFINE the purpose of a Navigation Brief. 10 - LIST the major components of a Navigation Brief.

## Slide 4
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Navy Amphibious Assault Ship Departs Naval Base – USS Boxer - YouTube

## Slide 5
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The process of getting a ship underway starts long before the ship ever leaves a berth.
-Navigation is comprised of a number of different processes.
-Some are done in order, some randomly, others infrequently.
-For the navigation team, ensuring the ship can safely depart a berth and proceed onto her operational commitments is of the utmost importance.

## Slide 6
Operational Messages
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Messages are sent continuously to advise higher commands about the whereabouts and operational capacity of the ships at sea.
-Before departure and arrival into port, there are messages that must be sent to ensure the ships can safely proceed into and out of port.
-The most common are the Logistics Request (LOGREQ) and the Movement Report (MOVREP).

## Slide 7
LOGREQ
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Logistics Request (LOGREQ) is a message that indicates what services you will require when you arrive or depart from a port. -These include your ETA, ETD, fuel, water, food, tug and pilot services. -This is critical to ensure you have everything you need when you arrive to a port. -The Supply Officer (SUPPO) will generate the message and route it through every Department Head (DH) for review. -The CO will sign and approve the message.

## Slide 8
MOVREP
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Movement Report (MOVREP) is a formatted message that tells where the ship is going, what the SOA is, where the waypoints are and what times they anticipate being at each waypoint.
-Submitted on the following occasions:
24-48 hours prior to sailing.
Upon arrival alongside in port.
When the ship has failed to sail.
+/- 4 hours of PIM

## Slide 9
MOVREP
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-PIM (Plan of Intended Movement) is built into the MOVREP, as this will show all of your planned waypoints and the intended time at each one. -In the MOVREP, a Navigator may also request Weather Report (WEAX) and an Optimum Track Ship Routing (OTSR) services.

## Slide 10
WEAX
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-If you request a WEAX in your MOVREP, you will receive daily forecast support for your location up to 72 hours out. -This service is usually provided by your nearest Fleet Weather Center (FLEWEACEN).

## Slide 12
OTSR
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-An OTSR is also requested from FLEWEACEN.
-Can be based on the ship’s operational limits.
-If severe weather is predicted to be encountered along your PIM which will exceed the ship’s limits, FLEWEACEN will propose a potentially safer alternate route that will remain outside the ship’s operational limits.

## Slide 13
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-With the operational messages covered, we must now take a look at the prevailing weather conditions before we get off the pier.
-Weather is of the upmost importance to a prudent navigator.

## Slide 14
Why Is Weather Important?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Typhoon Cobra AKA Halsey’s Typhoon 17 Dec 1944
Admiral William “Bull” Halsey-Commander 3rd Fleet

## Slide 15
Why Is Weather Important?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
80-100 kt sustained wind
120 kt gusts
40-50 ft high waves

## Slide 16
Why Is Weather Important?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
3 destroyers sunk
790 lives lost
9 warships damaged
100 aircraft lost

## Slide 17
Bad Weather
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Vessels collide in bad weather: https://www.youtube.com/watch?v=cC_eb7R3wPI Helicopter landing in rough seas: https://www.youtube.com/watch?v=NJIZTL2ZyEw Big seas: https://www.youtube.com/watch?v=tfEo6E6nElE Navy ship hit by 50 ft wave” https://www.youtube.com/watch?v=VYKBWldSBGg Carrier in big seas: https://www.youtube.com/watch?v=Z0Jzb8dfcC4

## Slide 18
Types of Weather
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Air mass: a large body of air with generally uniform temperature and humidity. As one moves across land and water, it eventually comes in contact with another air mass with different characteristics. The boundary layer between two types of air masses is known as a front. An approaching front of any type always means changes to the weather are imminent. There are four types of fronts: Warm, Cold, Stationary and Occluded.

## Slide 19
Warm Front
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Slides over and pushes the cold air -Longer -Brings lighter but longer lasting rain.

## Slide 20
Cold Front
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Moves faster -Pushes the warm air up -Shorter -Brings heavy rain and storms

## Slide 21
Stationary Front
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-When a cold front meets a warm front and none has the strength to push the other -No movement between the fronts -Rain may fall for many days

## Slide 22
Occluded Front
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-When a cold front catches a warm, and the warm air lifted off the ground -Can be cold or warm occluded depending on the temperature of the cold front catching -Has both cold and warm front characteristics (heavy rain on cold side / light rain on warm side)

## Slide 24
Pressure Systems (Northern Hemisphere)
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Circulation is curved due to Coriolis Force.
Circulation is on the opposite direction on the Southern Hemisphere.

## Slide 25
High Pressure
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Generally areas of dry, descending air.
-Good weather is typically associated with high pressure.

## Slide 26
Low Pressure
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Air flows into a low pressure area to replace rising air (unstable air).
-Usually brings increasing cloudiness and precipitation.
-Bad weather is typically associated with low pressure.
-Be on the lookout if you see:
Sudden decrease in pressure
Sudden decrease in temperature
Sudden change in wind direction

## Slide 27
Hurricanes
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Extremely low pressure system.
-Very dangerous.
-Avoid navigation around hurricanes.

## Slide 28
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-With weather covered, we must now identify the prevailing tide and current predictions from our departure and arrival port.
-Tide and currents can have a significant impact on how we safely navigate ships.

## Slide 29
Tides and Currents
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The proper understanding of tides and currents is essential to the navigator. -It is the difference between operational and navigational success and unnecessary loss of life and equipment. -History can be an amazing instructor…

## Slide 30
Gunther Prien’s U47 raid inside Scapa Flow bay 14th October 1939
HMS Royal Oak
Type VII B Unterseeboot 47

## Slide 31
Tide range > 20ft !
French Navy training ship Tigre grounded in Aber Wrac’h sound – 20th May 2009

## Slide 32
USMC invade Makin and Tarawa at neap tide
Notes: Makin Island Invasion: The assault troops were also surprised to discover that even though they were approaching the beach at high tide as planned, a miscalculation of the lagoon's depth caused their small boats to go aground, forcing them to walk the final 250 yards (230 m) to the beach in waist-deep water.
Tarawa

## Slide 33
Tides and Current
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Tide is the vertical rise and fall of ocean levels (bodies of water) caused by gravitational and centrifugal forces of the Moon and to a lesser extent the Sun. -Tides rise and fall. -Current is the horizontal movement of bodies of water resulting from the daily changes in tidal levels. -Currents Ebb and Flood.

## Slide 34
Tides
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-Flood tide – When the tide is rising -Ebb tide – When the tide is falling -Stand – The period when no change in water level is detected -Range of tide – Total rise or fall from consecutive low water to high water -High Tide- Maximum height of the tide -Low Tide – Minimum height of the tide.

## Slide 35
Tides
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-If the Earth were a perfect sphere without large continents, all areas on the planet would experience two equally proportioned high and low tides every lunar day. The large continents on the planet, however, block the westward passage of the tidal bulges as the Earth rotates. Unable to move freely around the globe, these tides establish complex patterns within each ocean basin that often differ greatly from tidal patterns of adjacent ocean basins or other regions of the same ocean basin. Dependent upon a body of waters dimensions it will have a natural period of oscillations classified into 3 categories: Semidiurnal Tide – Two high and two low waters each tidal day with relatively small inequality in consecutive high and low heights Diurnal Tide – One high and one low water each tidal day Mixed Semidiurnal Tide – Both semidiurnal and diurnal oscillations occur where the tide is typically characterized by a large inequality in the high-water heights, low-water heights or both.

## Slide 36
Tides
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 38
Spring Tide – When the Moon and Sun are in line with Earth the two influences act together, resulting in higher than average high tides and lower than average low tides
Neap Tide – When the direction from the Moon and Sun are 90 degrees apart the effect of the Sun partially counteracts the Moon’s influence, resulting in lower than average high tides and higher than average low tides
Tides

## Slide 39
Currents
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
Currents are the horizontal movement of bodies of water. It is a result of: Daily changes in tidal levels Steady blowing of the wind Normal flow of rivers from higher elevations to sea Long term climate or weather conditions -The direction of current is referred to as SET -The speed of the current is referred to as DRIFT

## Slide 40
Currents
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 41
Reversing Currents
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 42
Rotary Currents
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
A current with the direction of flow rotating through all points of the compass.

## Slide 43
Tide and Current Determination
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-In the past, Tide and Current Tables were needed to determine the tide and current information.
-Online services, such as NOAA Tides and Currents, allow real time access to the current tide and current levels for stations located around the United States.
-Applications such as Admiralty Total Tide allow mariners the ability to determine tide and current ranges at a variety of locations around the world.

## Slide 44
Tide and Current Determination
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-In the past, Tide and Current Tables were needed to determine the tide and current information.
-Online services, such as NOAA Tides and Currents, allow real time access to the current tide and current levels.
-Applications such as Admiralty Total Tide allow mariners the ability to determine tide and current ranges at a variety of locations around the world.

## Slide 45
Tide and Current Determination
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-In the past, Tide and Current Tables were needed to determine the tide and current information.
-Online services, such as NOAA Tides and Currents, allow real time access to the current tide and current levels.
-Applications such as Admiralty Total Tide allow mariners the ability to determine tide and current ranges at a variety of locations around the world.

## Slide 46
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-With tides and currents having been predicted, we must now identify the appropriate watch condition and the watchstanders that we will be required to have during a Sea and Anchor Detail or the evolution that occurs as we proceed into and out of port, as well as through restricted waters and into anchorage.
-This is a ship wide evolution, and the majority of the ship will be standing watch.

## Slide 47
Watch Conditions
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The U.S. Navy established watch conditions to state the various conditions of readiness and their purpose. CONDITION I – General Quarters, all hands to Battle Stations CONDITION II – Modified General Quarters, also called Condition II Damage Control to support DC efforts. CONDITION III – Wartime Cruising, generally 1/3 of the crew is on watch and strategic stations are manned or partly manned. CONDITION IV – Peacetime Cruising, provides adequate watch manning and provides personnel economy.

## Slide 48
Watch Conditions
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Ship will build watch bills for each Watch Condition. -CONDITION III – Wartime Cruising, is the most common watch condition while underway. -The NAVDORM dictates what watch standers a ship MUST have during the different phases of navigation, but based on a ship’s watch condition, they will stand up additional watches to support.

## Slide 50
Required Watchstanders
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy

## Slide 51
Getting Underway!
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-We have identified the watchstanders needed to conduct a successful Sea and Anchor Detail.
-Now we must put all our information together and brief it to the crew. This is called a Navigation Brief.

## Slide 52
The Navigation Brief
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The Navigation Brief is prepared to provide a plan for safe and prudent passage, including piloting in Restricted Waters. -Provides Commanders Intent, which means the Commanding Officer is able to directly state their intention for how the evolution will be conducted. -Written and briefed by the Navigator, with contributions from the 1st LT, Operations Officer, Chief Engineer and others. -It is signed by the Commanding Officer and retained onboard for one year. -The NAVDORM lists all the requirements needed for a brief. -IS REQUIRED WITHIN 24 HOURS OF A SEA AND ANCHOR DETAIL!

## Slide 58
Sample NAVBRIEF
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
-The following is a sample NAVBRIEF from USS LASSEN on INBOUND transit to NS Mayport on 30MAY2019.

## Slide 59
INBOUND NS MAYPORT FL
LTJG WILHELM
NAVIGATOR
30-MAY-2019

## Slide 60: REQUIRED ATTENDANCE Navigator
COMMANDING OFFICER | CDR VENTRESCA
EXECUTIVE OFFICER | CDR MALLORY
CHIEF ENGINEER | LT McCARTHY
OPERATIONS OFFICER | LT HANKS
NAVIGATOR | LTJG WILHELM
SENIOR QUARTERMASTER | QM1 CLANTON
SENIOR OPERATIONS SPECIALIST | OS1 CROCKETT
1st LIEUTENANT | ENS SONNIER
CICO | LTJG CASAS

## Slide 61: USS LASSEN (DDG 82) Outbound Mayport, FL Sea & Anchor Detail 29 MAY 2019
CO | 
XO | 
SWO | 

## Slide 62
INTERNAL COMMUNICATIONS Navigator
From Courage…Life
Controlling Station | Controlling Station | Net(s) Monitored
BRIDGE | CIC | Primary: NET 15 Secondary: 1MC Tertiary: NET 53 (MANEUVERING NET) Emergency: NET 91 (EMERGENCY NET)
BRIDGE | CCS | Primary: NET 15 Secondary: 1MC Tertiary: NET 53 (MANEUVERING NET) Emergency: NET 91 (EMRGENCY NET)
BRIDGE | FOC’SLE/ MIDSHIPS/FANTAIL | Primary: NET 56/1MC Secondary: NET 52 (LOOKOUT’s NET) Tertiary: NET 53 (MANEUVERING NET) Emergency: NET 91 (EMERGENCY NET)
BRIDGE | OIL LAB | Primary: X40J
CONNING OFFICER | HELM/HELM SAFETY | Primary: Verbal (In Pilot House) Secondary: 1MC Tertiary: NET 53 (MANEUVERING NET)
CONNING OFFICER | AFT STEERING SAFETY OFFICER | Primary: NET 53 via HELM SAFETY Secondary: 1MC Emergency: NET 91 (EMERGENCY NET)

## Slide 63
EXTERNAL COMMUNICATIONS Navigator
From Courage…Life
Controlling Station | Controlling Station | Net(s) Monitored
CO | MASTER OF VESSEL | Primary: BTB (CH 16, CH 12, CH 72) Secondary: Signal Flags Tertiary (Night): Flashing Light Safety Channel: BTB (CH 16)

## Slide 64
SEQUENCE OF EVENTS Navigator
Sequence of Events:
  0600: Station Sea & Anchor Detail
  0700: STJ/Pilot pick up
  0745: Moored
Operational Requirements:
  Condition of Readiness III
  Modified Zebra set main deck and below
Speed Restrictions:
Mariners are advised to enter/exit the Mayport Basin at slack water or at a recommended speed of 13 knots.
Tactical Condition:
  N/A
From Courage…Life

## Slide 65
WEATHER
Skies: SUNNY
Visibility: >7NM
Winds: SW 10-15 KTS
Temp: 94ºF/75ºF
Precipitation: 0%
Surface Duct: 6 Meters
ASTRONOMICAL DATA
Time Zone: 4Q
Sunrise: 0625
Sunset: 2022
Moonrise: 0409
Moonset: 1649
Illumination: 16%
WEATHER AND ASTRONOMICAL DATA Navigator
From Courage…Life

## Slide 66
TIDES: MAYPORT
Navigator
LASSEN WILL BE ARRIVING ON A FALLING TIDE. AT 0700 THE HEIGHT OF TIDE WILL BE 3.8 FT ABOVE CHARTED DEPTH
H | 0559 | 4.24FT | 1824 | 4.95FT
L | 1158 | 0.25FT |  | 

## Slide 67
FLOOD | 0424 | 1.46 | 1648 | 1.69
EBB | 1018 | -1.19 | 2254 | -1.09
CURRENTS: NS MAYPORT BASIN
Navigator
AT 0700 LASSEN WILL BE ARRIVING ON AN FLOOD CURRENT AT 1.0 KTS

## Slide 68
CHARTS
Navigator
VMS Plans:
  Layer Folio: APPROVED
  Chart Folio: APPROVED
  Voyage Plan: APPROVED
  Navigation Plan: APPROVED
Digital Nautical Charts:
  DNC 15, 39th Edition VDU 18/19
  DNC_H1508580 Jacksonville, FL
  DNC_A1508580 ST. Augustine, FL
  DNC_COA15B Northeastern Florida
  DNC_GEN15 Gulf of Mexico
  GPS Datum: WGS-84
Certification Dates:
  CNSS-14 NAVCERT:151417ZJUN18
  ISIC NSST EVAL: 24APR18
All charts corrected and compared through:
  NTM 22/19
  LNTM 21/19
  HYDROLANT 1581/19
Buoyage System: IALA Region B,
“Red Right Returning”
From Courage…Life

## Slide 69: INBOUND TRACK DATA ALL TURNS USE STANDARD RUDDER Conning Officer
From Courage…Life
LEG | TURN | COURSE | DISTANCE | SPEED
1-2 | NO TURN BEARINGS | Steady up on 280°T/286°M | 10.40 NM | 10kts
2-3 | NO TURN BEARINGS | Left Standard Rudder 277°T/283°M | 10,960 yds | 10kts
3-4 | TB-“C” 221°T/326°R (STJ Tower with light on top) TR- “R5” 1,966 yds | Left Standard Rudder 255°T/261°M | 2,721 yds | 5-10kts

## Slide 70
C- 277°T/283°M
D- 10,960 YDS
S- 10 KTS
C- 280°T/286°M
D- 10.40 NM
S- 10KTS
Pilot Pick Up IVO STJ

## Slide 71
TR “R5”
1,966 yds
Channel Width: 260 YDS
TB “C”
221ºT/326ºR
ST JOHN’S LIGHT
Line of Demarcation
C- 277°T/283°M
D- 10,960 YDS
S- 10 KTS

## Slide 72
Turning Basin Width: 650 YDS
Pier Heading: 285/105°T
C- 255°T/261°M
D- 2,721 yds
S- 5-10 KTS
Degaussing Range
Range Lights

## Slide 73
R4
G3
R6
G5
R8
G7
JUNCTION BUOY
GRG
G1
R4
R2
G1A
BOUY INFO

## Slide 74
TRANSIT INFORMATION Navigator
Emergency Anchorages:
  Anchor using 5x the water depth for shots used.
  3 SHOTS
Bottom type: Sand and Mud
15 fathoms in each shot
1 shot = 90 FT
Designated Shoal Water:
  36 FT (11m) BOLD BLACK soundings on DNCs Deepest Projection
Average Depth of Water for Transit:
  Average charted depth: 38-50 FT
From Courage…Life
Transit information:
A deep channel leads along the inshore end of the south jetty to the basin. It is marked by a 255° lighted range and unlighted buoys. Due to the relatively short distance between the lights of the range, sensitivity is poor. Mariners are advised to use the range with caution.

## Slide 75
GROUND TACKLE 1ST LT
Mooring Config: 10 Standard (Spectra) Mooring Lines Singled
Ready Anchor: Centerline - At the Dip
Secured with riding stopper and brake Chain compressor engaged
Wild cat disengaged
12 shots available, 12th shot is Red in color for
Danger and the 11th shot is yellow in color for
Warning. All personnel will stand clear of the
anchor when the warning shot appears. 1 shot
consists of 15 Fathoms or 90 Feet. 1 fathom is equal
to 6 feet.
Bottom type: Sand and Mud
Accom. Ladder: SERMC Repairs
Windlass: Tested operational, then disengaged
Ready lifeboat: ZEKE
Boats in Water: None
From Courage…Life

## Slide 76
GROUND TACKLE 1ST LT
From Courage…Life
EMERGENCY: In the event of an emergency, Bridge will order “let go of the anchor”.
1. Foc’sle will trip the riding stopper, then disengage the chain compressor. Rigger will verify that it is open.
2. Once chain compressor is open, POIC will then say, “Brake man release the brake.”
3. At this point, POIC will be giving status reports to the bridge on how the anchor is tending and wait for further orders.

## Slide 77
GROUND TACKLE 1ST LT
From Courage…Life
MIN REQUIRED LENGTH OF CHAIN: 180 FT

## Slide 78
Emergency Anchorage: Outside anchorage berths lie north-northeastward of the St. John's River entrance jetties. There are four carrier anchorages (A though D) and six destroyer anchorages (1 through 6).
CARRIER
A-D
EMERGENCY ANCHORAGE LOCATIONS Officer of the Deck
From Courage…Life
DESTROYER
1-6
1
2
3
4
5
6
D
C
B
A

## Slide 79
LINE COMMANDS 1ST LT
From Courage…Life
COMMAND | MEANING
Pass one (or Number One) | Send line number one over to the pier. Place the eye over the bollard or cleat but do not take a strain.
Slack (slack off) the bow line (number one) | Pay out the line specified, allowing it to form an easy catenary.
Take a strain on one (or number one) | Put number one line under tension.
Take the slack out of three (or number three) | Heave in on number three line but do not take a strain.
Ease three | Pay out number three line enough to remove most of the tension.
Avast heaving | Stop heaving (taking in).
Check three | Hold number three line, but not to the breaking point, let the line surge as necessary.
Hold two | Take enough turns so that number two line will not surge.
Single up | Take in all lines except a single standing part to each station, preparatory to getting underway.
Stand by your lines | Man the lines, ready to cast off or moor.
Take in one (or number one) | Retrieve line number one after it has been cast off.
Cast-off | A command to those tending the mooring lines on the pier or on another ship to disengage or throw off the lines from over the bollards or cleats.
REFERENCED FROM NSTM 582 MOORING AND TOWING TABLE 582-2-5 LINE HANDLING COMMANDS | 

## Slide 80
MOORING CONFIGURATION 1ST LT
From Courage…Life

## Slide 81
LINEHANDLERS 1ST LT
From Courage…Life
FO’C’SLE POIC | LINE 1 | LINE 2 | LINE 3
BM2 SHOTWELL | LINE CAPTAIN BM2 JONES | LINE CAPTAIN BM2 TIPPIT | LINE CAPTAIN BM3 ALEXANDER
 | BMSR FORDHAM | IT3 FAULKNER | CTT2 ZAMORA
 | SN MCCOY | IT2 BRAMHALL | CTR2 KOCHAN
 | SA SUAREZ | ITSN MOORE | CTT2 DURHAM
 | SA LEONARD | ITSR GREGG | CTR3 VANBLARCOM
 | SA SCHWANZ | IT3 SELLERS | CTT3 OTERO

## Slide 82
LINEHANDLERS 1ST LT
From Courage…Life
FANTAIL POIC | LINE 4 | LINE 5 | LINE 6
BM2 LAMBERT | LINE CAPTAIN ET3 SOBOTA | LINE CAPTAIN STG2 TIDMORE | LINE CAPTAIN FCA1 PARKER
 | ET3 METREJON | STGSA BROWN (U/I) | FCA3 DUPEPE (U/I)
 | ET3 CARLSON | STG3 GLENN | FCA3 ARMAS (U/I)
 | ET2 HILARIO | STGSN GRIFFIN | FCA2 ZYDUCK
 | IC3 VILLA | STGSA BELL | FCA3 WOOD
 | ET2 GRAEBER | STGSN ELLIS | FCA3 RICHEY
 | ET2 MORIN |  | FCA3 BONDOC
 |  |  | FCA3 ROSADOROSARIO

## Slide 83
LINEHANDLERS 1ST LT
From Courage…Life
MIDSHIPS POIC | LINE 7
SH2 KROLL | LINE CAPTAIN SH2 KROLL
 | CS2 BALLESTEROS
 | SH2 OMUNYIDDE (U/I)
 | CS3 LOMBARDI
 | SHSA NAHNSEN (U/I)

## Slide 84
Safety brief will be conducted by the Safety Officers once Sea and Anchor detail is manned.
  FO’C’SLE – BMC DICICCO (Q)
  MIDSHIPS - LT KING (Q)
  FANTAIL - ETC MORGAN (Q)
SAFETY 1ST LT
From Courage…Life

## Slide 85
Traffic (Operations Officer)
)
MOVEMENTS Operations Officer
DATE SHIP TIME FROM TO
30MAY USS LASSEN 0700 SEA D-1

## Slide 86: SPECIAL CONSIDERATIONS/EVENTS Operations Officer/CICO
Harbor Special Events:
None
Media Coverage:
None
Hot Area(s):
30MAY
W-136E 0000Z-0400Z GUNX HSM-70
W-137L 0045Z-0315Z GUNX HSM-60
Flight Operations:
Lear DTE

## Slide 87
TUGS AND PILOTS Navigator
Communications:
  VHF-FM channels 12, 13 and 16, working channel is 12
Pilot Pick Up:
  Mayport Basin
Pilot Drop Off:
  Pierside
Tug Characteristics:
  Z DRIVE PODS PROPULSION RATED AT 4,000 SHAFT HORSEPOWER

## Slide 88
NAVIGATION EQUIPMENT
Navigator
From Courage…Life
Fwd WSN-7 | UP | SPS 67 | UP
Aft WSN-7 | UP | SPS 73 | UP
Centerline Gyro | UP | SPA 25G Bridge | UP
Helm Gyro | UP | SPA 25G CIC | UP
Aft Steering Gyro | UP | VMS | UP
Fwd GVRC | UP | Fathometer | UP
Aft GVRC | UP | DFGMC | UP
DAGR (GPS) | UP | AIS | UP
ENL | UP | DEML | UP
SHIP’S WHISTLE | UP | FURUNO | UP
NOTES: NTR

## Slide 89
GYRO ERROR Navigator
From Courage…Life
Gyro error: 0.2ºE by Azimuth of the Sun on 28MAY19
Repeater Errors:
Underway Restrictive: (<1º of error )
-Centerline: 0.0º
  -Helm: 0.2ºE
  -Aft Steering: 0.0º
  Not underway Restrictive:
  -Port: 0.1ºW
  -Stbd: 0.0º

## Slide 90
VMS Navigator
Primary:
HDG: FWD RLGN
COG: FWD GVRC
SOG: FWD GVRC
STW: FWD RLGN (DEML)
POS: FWD GVRC
Secondary:
HDG: AFT RLGN
COG: AFT GVRC
SOG: AFT GVRC
STW: AFT RLGN (DEML)
POS: AFT GVRC
EMERGENCY PROCEDURE:
In the event of a complete loss of GPS inputs, the Bridge will maintain an electronic plot w/ visual/ radar inputs from DAGR information into the ENL or manual inputs into VMS.
VMS Order of Succession
NAV 1
CONN
NAV 3 (Chart Rm)
NAV 2 (CIC)
NAV 4 (CO)
ENL
From Courage…Life

## Slide 91
RADAR CONFIGURATION Junior Officer of the Deck
From Courage…Life
Setup will be IAW CO’s Standing Order # 17
Watchstanders will continually assess the following SPS-73 radar settings based upon contact situation, and configure them as necessary.
  Initial Set-up:
    Range Scale – 1.5NM - 3 NM
    Pulse Width – Short
    Display Heading Mode – North Up
    Vectors – True
    Radar Gain – 35%
    Track Sensitivity – 80%
    Sensitivity Time Control (STC) – 10%
    Fast Time Constant (FTC) – 5%
Watchstanders will continually assess the following SPS-73 radar settings based upon lighting considerations, and configure them as necessary.
  Initial Set-up:
    Radar Brightness – Daylight
    Menu Brightness – Daylight

## Slide 92
  GTMs
    1A/1B/2A/2B GTMs Online
    Thrust Control on the Bridge
  GTGs
    NR1 and NR3 GTGs online in parallel. NR2 GTG running in offline
  DEGAUSSING:
    Energized
  STEERING GEAR:
    HPUs: 1B/2B HPUs online, 1A/2A HPUs in standby
    Steering control on the Bridge in BACKUP MANUAL
    Steering Gear Checks: completed 30MAY19
    OOC/Degraded:
    NTR
ENGINEERING PLANT STATUS Plant Control Officer
From Courage…Life

## Slide 93
ENGINEERING EQUIPMENT
Plant Control Officer
From Courage…Life
1A HPU | UP | 2A HPU | UP
1B HPU | UP | 2B HPU | UP
EPCC | DEG | 1A/2A LCU | UP
PACC | UP | 1B/2B LCU | UP
PORT SHAFT- NR2 SCU | UP | PORT RUDDER | UP
STBDSHAFT- NR1 SCU | UP | STBD RUDDER | UP
FWD CRP | UP | BRIDGE CONTROL UNIT | UP
AFT CRP | UP | AFT STEERING UNIT | UP

## Slide 94
Restricted Maneuvering Doctrine is designed to ensure continuity of ship’s propulsion and electrical power when the safety of the ship depends upon our ability to maneuver.
Restricted Maneuvering Doctrine intentionally risks damaging equipment by DELAYING or DEVIATING from EOCC in situations where immediate/controlling action places the ship at greater risk.
Set by Commanding Officer when:
      Operating in restricted waters
Take all normal EOCC actions, but require CO’s permission to prior to
securing:
    Last GTM on EITHER shaft, last GTG, last STEERING GEAR UNIT
    Securing the source of a leak for F/O to a GTM or GTG, L/O, CRP, or flooding
    Electrically or mechanically isolating any equipment or systems
    Electrically isolating a switchboard
    Last ENGINE on EITHER shaft will be placed in BATTLE OVERIDE
    The last LPAC online will be placed in BATTLE OVERIDE
    Thrust control will remain in the pilothouse for all casualties
ENGINEERING CASUALTIES: Plant Control Officer
From Courage…Life

## Slide 95: SPECIAL CONSIDERATIONS Navigator
HONORS: Passing Honors shall be rendered between the hours of 0800 and sunset for vessels close board (600 yds for ships, 400 yds for boats). Pursuant to NTP-13 passing honors are required between ships that are either underway or anchored.
●● Attention to Port
WHISTLES: ● Attention to Stbd
● Hand Salute ●● Ready-Two ●●● Carry On
Expected Honors: None
Flag Officer Movement: None
Visitors: Ship Riders
Harbor Exercises: None
Debrief Schedule: After Sea and Anchor
Uniform: Clean Navy Working Uniform
From Courage…Life

## Slide 96
Assessment Zone
  Visual Range
Warning Zone
  1000yds (Small Boat)
  6000yds (Low Slow Flyer)
Threat Zone
  400yds (Small Boat)
  3000yds (Low Slow Flyer)
FORCE PROTECTION PERIMETERS Gun Directing Officer
WARNING ZONE
MT 503
MT 504
MT 507
MT 508
THREAT ZONE
From Courage…Life
ASSESSNENT ZONE

## Slide 97
SCAT Manned and Ready
  Team on station in proper PPE
  Weapons mounted in Condition 4.
    Ammunition on station, chamber empty, action closed, safety on
  COMMS checks SAT
CSW mounts report estimated bearing and range of all contacts within visual range to the GDO and search for signs of hostile intent.
  Signs of Hostile Intent:
    Presence of weapons, evasion of picket boats, approaching at high speed, multi-contact coordinated approach, failure to comply to directions/warnings, and threats over BTB.
SMALL CRAFT ACTION TEAM Gun Directing Officer
From Courage…Life

## Slide 98
“Track”
  Visually track contact
“Cover”
  Train mount towards target
“Make Ready”
  Condition 3 to Condition 1, chamber round.
“Cease Fire”
  Cease engagement of target.
“Batteries Release”
  Destructive Fire
STANDARD COMMANDS Gun Directing Officer
From Courage…Life

## Slide 99: Threat and Error Management Officer of the Deck
Mission Effectiveness
Threats
Errors
Incident/Accident
Undesired
Ship
State
Prepare
Repair
Recover

## Slide 100: Threat and Error Management Officer of the Deck
Incident/ Accident:
Collision/Grounding
Undesired Ship State:
Man overboard, near-collision, near-grounding, loss of steering, loss of propulsion
Threats:
Equipment casualties (steering, propulsion, navigation system, communications, radar, anchor), surface traffic, fatigue, weather and visibility
Errors:
Loss of BRM, Improper responses to casualties (procedural, communication, proficiency, decision, intentional non-compliance)
RECOVER
REPAIR
PREPARE

## Slide 101
From Courage…Life
Threats
Equipment casualties (steering, propulsion, navigation system, communications, radar, anchor), surface traffic, fatigue, weather and visibility
PREPARE BY:
  Conducting the Chart Review and the Navigation Brief.
  Reviewing and signing all line items on the Getting Underway Checklist.
  Performing Pre-Underway Maintenance.
  Understanding predicted weather and preparing accordingly (i.e. Low Visibility Procedures IAW CO’s Standing Order # 7).
  Conducting safety briefs on station.
  Ensuring qualified personnel are standing assigned watchstations.
  Properly training junior watchstanders how to effectively perform the duties of the watchstations.
  Utilizing proper bridge and station resource management.
  Utilizing all available bridge tools (AIS, ARPA, VMS, etc.) to ensure the safe navigation of the ship.
  Following COLREGS, CO’s Standing Orders, and other applicable manuals/publications.
  Ensuring all watchstanders are well rested and alert for watches.

## Slide 102
From Courage…Life
Errors
Loss of BRM/SRM, Improper responses to casualties (procedural, communication, proficiency, decision, intentional non-compliance)
REPAIR BY:
  Quieting the bridge and refocusing the watch team.
  Following COLREGS.
  Utilizing Standard Commands.
  Minimizing bridge traffic.
  Shifting to alternate equipment
    Loss of Comms (ext): Shift to alternate equipment: BTB, Signal Flags, 1MC, Flashing Light, Bullhorn
    Loss of Comms (int): Shift to alternate comms path: 1MC, Secondary and Tertiary Nets
    For a Loss of GYRO, shift from GYRO 1 to GYRO 2. If True Heading is not regained, shift to DFGMC and utilize relative plot on VMS.
    For a loss of RADAR, shift to alternate radar and/or shift to alternate repeater.
  Shifting to alternate sensors for a loss of VMS sensor inputs and understanding the VMS order of precedence.
  Having senior safety observers ensure proper response to casualties.
  Having qualified personnel on standby to repair equipment casualties.
  Making up tugs to proceed to emergency anchorage.
  Utilizing the 1MC to communicate to the crew.

## Slide 103
From Courage…Life
Undesired Ship State
Man overboard, near-collision, near-grounding, loss of steering, loss of propulsion
RECOVER BY:
  For a Man Overboard, conducting Man Overboard procedures IAW the Man Overboard Bill.
  For a Loss of Steering:
    HELM SAFETY will report to OOD: “I have lost control of PORT/STBD/both rudder(s).”
    HELMSMAN shift to standby steering gear units, TEST for POSITIVE CONTROL.
    If control is not regained, depress “STEERING CASUALTY ALERT SWITCH” pushbutton.
    After Steering will MATCH RUDDER, TAKE CONTROL, and TEST for POSITIVE CONTROL.
    If control is not regained, shift to 2A LCU.
    If control is still not regained, shift to 2B LCU.
    If control is still not regained, notify the OOD and recommend steering by engines to emergency anchorage
  For a Loss of Propulsion:
    Make up tugs and proceed to emergency anchorage.
  For a Near-Collision:
    Utilize a safe heading and safe speed.
    Proper contact management.
    Staying in compliance with COLREGS.
    Communicating with other vessels (B2B, sound signals).
  For a Near-Grounding:
    Listening to NAV’s Report.
    Reviewing your chartlet and knowing where shoal water lies.

## Slide 104
From Courage…Life
Undesired Ship State:
Man Overboard
Threats | Prepare
Personnel topside Lack of SRM Weather/Visibility Fatigue | Safety Brief conducted on station. Rested and qualified personnel on station. Brief weather conditions and dress appropriately (chemlights, foul weather gear, MK 1 and KAPOCs).
Errors | Repair
Noisy Station/Bridge Unnecessary personnel on station | Refocus watch team. Utilize Standard Commands Minimize traffic on station.
Undesired Ship State | Initial RAC | Recover | Final RAC
Man Overboard | 2 C,I | MOB Procedures IAW MOB Bill Tug/Pilot Recovery Ship RIB Recovery Ship Foc’sle Recovery | 3 D,I
Probability | A: Likely to occur B: Probably will occur C: May occur D: Unlikely to occur | Severity | Probability |  |  |  |  | RAC 1 – Critical 2 – Serious 3 – Moderate 4 – Minor 5 – Negligible
 |  |  |  | A | B | C | D | 
 |  |  | I | X | X | X | X | 
Severity | I: Death II: Serious Injury III: Minor Injury IV: Minimal Threat |  | II | X | X | X | X | 
 |  |  | III | X | X | X | X | 
 |  |  | IV | X | X | X | X | 

## Slide 105
From Courage…Life
Undesired Ship State:
Loss of Steering
Threats | Prepare
Steering Casualty Lack of Procedural Compliance | Safety Brief conducted on station Performing Pre-underway maintenance Qualified watchstanders and safety observers
Errors | Repair
Improper Response to a Casualty | Senior safety observers ensure proper response. Utilize Standard Commands
Undesired Ship State | Initial RAC | Recover | Final RAC
Loss of Steering | 2 C,I | Utilize immediate and controlling actions from Master Helmsman, Helm Safety Officer and Aft Steering Officer. Make up tugs Proceed to emergency anchorage | 3 D,I

## Slide 106
From Courage…Life
Undesired Ship State:
Loss of Propulsion
Threats | Prepare
Propulsion Casualty Lack of Procedural Compliance | Safety Brief conducted on station Performing Pre-underway maintenance Qualified watchstanders and safety observers
Errors | Repair
Improper Response to a Casualty | Senior safety observers ensure proper response. Utilize Standard Commands
Undesired Ship State | Initial RAC | Recover | Final RAC
Loss of Propulsion | 3 C,II | Utilize immediate and controlling actions from Master Helmsman, Helm Safety Officer and Aft Steering Officer. Make up tugs Proceed to emergency anchorage | 4 D,II

## Slide 107
From Courage…Life
Undesired Ship State:
Near Collision (In Extremis)
Threats | Prepare
Surface Traffic Weather/Visibility Navigation System Casualty Loss of BRM Lack of Procedural Compliance Fatigue | Watchstander proficiency and adherence to COLREGS Briefing expected weather/illumination Senior safety observers Utilizing all bridge tools (AIS, ARPA) Crew rest/circadian rhythm
Errors | Repair
Loss of Bridge Resource Management Improper Response to a Casualty | Refocus watch team and minimize bridge traffic Utilize Standard Commands Safe heading/speed Proper contact management Identify improper response
Undesired Ship State | Initial RAC | Recover | Final RAC
Near Collision (In Extremis) | 2 C,I | Safe heading/ speed Proper contact management Compliance w/ RoR Communications with other vessel (B2B, sound signals) | 3 D,I

## Slide 108
From Courage…Life
Undesired Ship State:
Near Grounding (In Extremis)
Threats | Prepare
Surface Traffic Weather/Visibility Navigation System Casualty Loss of BRM Lack of Procedural Compliance Fatigue | Watchstander proficiency and adherence to COLREGS Briefing expected weather/illumination Senior safety observers Utilizing all bridge tools (AIS, ARPA, VMS, etc.) Crew rest/circadian rhythm
Errors | Repair
Loss of Bridge Resource Management Improper Response to a Casualty | Refocus watch team and minimize bridge traffic Utilize Standard Commands Safe heading/speed Proper contact management Identify improper response
Undesired Ship State | Initial RAC | Recover | Final RAC
Near Grounding (In Extremis) | 3 C,II | Safe heading/ speed Proper navigation reports | 4 D,II

## Slide 109: Individual Risk Management Navigator
Watch Station / Name | Watch / Rest | Experience | Weather | Equipment | IRM
CO / CDR VENTRESCA | 2 | 4 | 4 | 3 | 13
XO / CDR MALLORY | 2 | 4 | 4 | 3 | 13
NAV / LTJG WILHELM | 2 | 4 | 4 | 3 | 13
OOD / LTJG EATON | 2 | 4 | 4 | 3 | 13
JOOD / LTJG ANTOMMARCHI | 2 | 4 | 4 | 3 | 13
JOOW / ENS COLLINS | 2 | 3 | 4 | 3 | 12
CONN / ENS WESEMAN | 2 | 2 | 4 | 3 | 11
CICWO / ENS FRANCIS | 2 | 3 | 4 | 3 | 12
SHIPPING OFFICER / OS3 LARSON (I) | 2 | 3 | 4 | 3 | 12
PILOTING OFFICER / OS2 HEILMAN (I) | 2 | 4 | 4 | 3 | 13
CSOOW / FCA2 LUNA | 2 | 4 | 4 | 3 | 13
EOOW / MMC SCOTT | 2 | 4 | 4 | 3 | 13
OVERALL: |  |  |  |  | 12
Watch to Rest Ratio:
4 – No watch leading into event, 7 hrs sleep in last 24 hrs
3 - Stood a full watch before event, 7 hrs sleep in last 24 hrs
2 – Between 5 and 7 hrs sleep in last 24 hrs
1 – Less than 5 hrs sleep in last 24 hrs
Experience:
4 – 11 or more details in last 3 mos
3 – 5-10 details in last 3 mos
2 – Less than 5 details in last 3 mos or U/I
1 – First time as qualified watchstander
Weather:
4 – Good
3 – Moderate
2 – Significant
1 – Heavy
IRM Code:
<8: Critical
8-10: Serious
11-13: Moderate
13-14: Minor
15-16: Negligible
Equipment:
4 – All Equipment operational
3 – Moderately degraded Equip
2 – Severely degraded Equip
1 – Primary / backup Equip OOC
INBOUND MAYPORT

## Slide 110
  Previous S&A
Great job running the checklist!
Noisy bridge. Need to focus on hierarchy of voices.
Confusion on taking in Line 9.
Delay in underway time due to IRAT checks.
Turn from 075°-097° was called late…still ended up about 15 yards right of track.
LESSONS LEARNED Navigator
Trending Issues
Standard Line Commands.
Level of noise on bridge.
Turn from 075°-097°…
LASSEN drives the ship and U/W time.
Safety of Navigation is ship’s business!
From Courage…Life

## Slide 111: QUESTIONS?

## Slide 112
NAVIGATOR
____________________
EXECUTIVE OFFICER
_____________________
COMMANDING OFFICER
_____________________
APPROVAL
Commanding Officer

## Slide 113
Enabling Objectives
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy
1 – DESCRIBE the following operational messages: LOGREQ, WEAX, and MOVREP. 2 - UNDERSTAND the impact of hazardous weather conditions on surface and flight operations. 3 – DESCRIBE different weather fronts and the difference between high and low pressure systems. 4 - DESCRIBE the importance of understanding Tides and Currents. 5 - DESCRIBE the causes of tides. 6 - DESCRIBE the two main types of currents and the two main types of tidal currents. 7 - DESCRIBE the different types of watch conditions. 8 - DETERMINE the appropriate watchstanders needed for Restricted Waters, Piloting Waters, Coastal Waters and Open Ocean Transits IAW the NAVDORM. 9 - DEFINE the purpose of a Navigation Brief. 10 - LIST the major components of a Navigation Brief.

## Slide 114
Questions?
Operations Officer I HMS PROTECTOR A173 I The Ice Patrol Ship
NN220 – Fundamentals of Navigation
SEANAV I United States Naval Academy